Deterioration and restoration of Dutch small rivers and brooks, especially of its submerse vegetation

- developments and perspectives in respect to EU Water Framework Directive –

DRAFT WITHOUT FIGURES

By: Dr. H.W.J. van Dijk, The Netherlands

## Paper on basis of presentation during the symposium “Complex systems under extreme conditions” (Ergaki / Siberian Federal University (Krasnoyarsk) June 27, 2008)

# Contents

## Introduction: complex systems under extreme conditions?

## Origin of Dutch brooks

## Relevant developments 1945 - now

## Regional water management in the Netherlands

## Research on aquatic macrophytes (methodology, first results)

## Changes of aquatic flora 1971 - now

## EU Water Framework Directive

## Case: Luronium natans

## Perspectives of Dutch brooks and its plants

References

Annexes (2)

## 0. Introduction

# The theme of the symposium is “Complex systems under extreme conditions”. This brings us to several questions: Are Dutch brooks systems? Are these systems complex? And are these systems under extreme conditions?

- Are Dutch brooks systems?

The answer is a general yes, but the working out of this question is variable depending on discipline and political view. For the old-fashioned agricultural engineer a Dutch brook only was a system for discharge of superfluous water and for storage in times of drought. The brook was simplified to the application of some hydraulic and hydrological formulaes. For the urban engineer of the seventies of the 20th century the brook only was a system for discharge of effluent from waste water plants.

## For the ecologists working scientifically on brooks since about 1960 natural brooks are very complex ecosystems.

## For many modern Dutch politicians nature values (including roles for outdoor recreation), urban as well as agricultural functions must be fulfilled by brooks. However, with the planning of brooks restoration and maintenance often short-term economic interests are still dominating.

- Are Dutch brooks complex systems?

The ecological complexity of brook ecosystems is determined by many factors. Below we only mention some of them shortly:

### There is a hierarchy of many determining principles on several scales: climate -> landscape -> soil condition -> hydrology -> water chemistry -> ecosystem -> species composition.

### In mesotrophic and good hydrological conditions the ecosystem is complex on basis of many natural gradients: seepage in and along the banks, sedimentation-erosion in the lower parts, dynamics of benches, interactions between wells, brooks, rivers, brook banks, variation in natural subsoil. Because of these gradients the species composition is rich and diverse (Verdonschot 1995).

### There are very complex interactions between the many groups of organisms which occur in natural circumstances: fishes, larvae of dragonflies, stoneflies, respectively mosquitoes, water bugs, macrophytes, algae a.o. (Nijboer 2006).

### In the lowland brooks of Northwestern-Europe many hundreds of regionally distributed and very specialized species per group of organisms can be found in the locally still consisting original natural circumstances.

# Nowadays there is also a political complexity around Dutch brooks. This complexity can be illustrated by following.

### Politicians order engineers and ecologists to find good solutions by integrated approaches (Dutch “polder model” to come to satisfying compromise solutions)

### The “polder model” worked well during the 80’s and 90’s but after 2000 a growing distance between ecological and technical solutions may be observed

### However the politicians are speaking about sustainable developments, there is still a strong focus on “end-of-pipeline” solutions instead of choosing for more fundamental solutions for environmental problems.

# Are Dutch brooks under extreme conditions?

## The answer is a very clear YES because of following reasons:

## The Netherlands is a very small country with a large population (500 inhabitants / km2; compare to Siberia with a population density of approx. 0.5 / km2 !)

## The very intensive agriculture in the Netherlands which is 3d largest exporter of agricultural products in the world (coming from only 30,000 km2)

## Quick urbanizing developments

## During last decades hundreds of agricultural and urban engineers with wrong (non-ecological) principles and politicians who generally prefered short-term economical profit above sustainability

# In this paper the main question is: HOW FAR CAN WE COME WITH AN INTEGRATED APPROACH OF RESTORATION AND MAINTENANCE OF DUTCH BROOKS BY URBAN AND AGRICULTURAL ENGINEERS AND ECOLOGISTS ???

# 1. Origin of Dutch brooks

The Netherlands are situated in the delta areas of four large to medium-scale rivers (Rhine, Meuse, Scheldt and Ems; see figure 1). This location at the end of river systems was automatically combined with a long-term struggle of the inhabitants of Europe’s “Low Lands” against sea and floods from rivers. This struggle determined the Dutch landscape and its inland water systems to a large scale. In the western and northern part of the Netherlands stagnant water systems (lakes, former sea creaks and artificial ditches and canals) are now the dominating elements in the water system. Large areas here are below sea-level and can only been preserved as places for human life by constructing and maintaining the large systems of ditches and canals for the discharge of precipitation water and by large pumping stations which bring the water from the discharge canals into the sea.

During the Middle-ages the Dutch rivers were still very dynamic but they are fixated more or less by man during last centuries. The small rivers and brooks we are discussing about in this paper were even more dynamic than the larger rivers until the 19th century. The small rivers and brooks with more or less flowing water are nowadays restricted to mostly sandy areas in the east and the south of the Netherlands.

FIGURE 1. The Netherlands situated in the delta area of four rivers.

## In former times (until 1.700 – 1.900 aC) many marshes and bogs covered large areas in the Netherlands, in the lower parts as well in the higher parts. In these areas the water discharge mainly occurred by marsh and peat flow systems. During approx. 1,500 – 1,920 aC first small-scale intensifications of agriculture were carried out. These intensification works started with the drying out and/or complete removing of natural peat layers and bogs until the sandy sub-soils were reached. The result were large sandy surfaces especially in the more hilly south and east of the Netherlands (Figure 2). During this development the original marsh flow systems developed to free flowing brooks. This development reduced the hydrological retention of the areas concerned. All these developments which occurred during last centuries make it difficult to determine the natural status of Dutch brooks, one of the administrative obligations of the EU Water Framework Directive.

FIGURE 2. The Dutch brooks are situated in the eastern and southern part of the Netherlands

2. Developments 1945 - now

## After the Second World War the intensification of Dutch agriculture became more rapid then ever before. The European Union strongly supported the enlarging of the scale of the Dutch landscape to enable this intensification. Many billions of subsidies coming from Brussels have been used for this purpose. In fact a complete adaptation of the landscape occurred to enable a quick growth of agricultural production: intensive drainage per field, less trees and little forests in the agricultural areas, and enlarging the fields (Figure 3). At the same time there was an intensifying use of fertilizers, which caused a strong eutrophication of groundwater and surface water. During the seventies many grain fields have been changed into maize fields. Later the same happened to many Dutch meadow-lands. The maize yields are used for feeding of cattle, especially millions of pigs. The “advantage” of the new maize species introduced was that the fields where they were cultivated, could be used for the deposition of enormous amounts of superfluous dung, produced by pigs and chickens. Since then the concentrations of nitrate and phosphate in groundwater and surface water strongly increased.

FIGURE 3.

Around 1960 most Dutch brooks had been completely rebuilt to a new artificial and uniform concept to enable a maximum discharge of precipitation in autumn and winter. This development took only 20 – 30 years. By many weirs constructed in the brooks the water storage capacity of the brooks was enlarged artificially for the needs of agriculture in dry summer periods. In fact the formerly natural brooks with rather high velocities of the water flow had been reshaped into almost artificial discharge and storage canals for agricultural and urban areas.

For the water quality it was important that during 1970 a new law against surface water pollution was established. Because of this law many new sewage systems and waste water treatment plants have been constructed. Whereas the waste water treatment of urban areas has been strongly improved since 1970, the diffuse pollution from agriculture strongly increased until around 1990. The result was that the saprobic status of the brooks improved after 1970: the organic content of effluents dropped resulting in a more optimal fluctuation of oxygen contents. During 1970 – 1990 generally phospate contents decreased, but nitrate concentrations in surface water and groundwater still increased because of agricultural activities.

Initiated by the EU Nitrate Directive (protection of groundwater against nitrate pollution) since 1990 there is a new:development to an equilibrium status for the use of fertilizers in agriculture. The aim for 2030 is an equilibrium situation between fertilizing and the use of P, N and K by crops. Meanwhile the subsoil and the groundwater is so saturated with nutrients that it will take some more decades to finish the strong eutrophication of brooks.

The ecological changes of Dutch brooks between 1850 and 1960 are illustrated by following tables and accompanying pictures.

# Brook around 1850

In figure 4 an undisturbed part of River Dinkel is shown. This was the general look-like of brooks around 1850 in a landscape of still mall-scale agriculture. The general characteristic of these brooks were as follows:

## Erosion and sedimentation: mozaic of many various biotopes within ecosystem

## Free discharge, free fish migration

## Summer: continuous (low) flow because of natural retention groundwater

## Winter: not too large discharge peaks (buffering hydrological system upstream)

## Water quality: mesotrophic, little organic sediment, high oxygen content, clear water

# FIGURE 4. Brook around 1850 (Dinkel)

# Brook around 1960

In figures 5 and 6 completely disturbed parts of rivers Dinkel and Vechte –both crossing the German-Dutch border- are shown. During the fifties the whole landscape which surrounds this part of River Dinkel has been adapted to large-scale agriculture. The general characteristic of this type of brooks, which are completely adapted to the new agricultural standards for water discharge and water storage, were as follows:

## No erosion and sedimentation, monotonous biotope (like an artificial ditch or canal)

## No free discharge: many weirs, fish migration reduced

## Summer: (almost) stagnant water because of reduction of retention water system

## Autumn/winter: more large discharge peaks because of less hydrological buffering

## Water quality: eutrophic-hypertrophic, much organic sediment, oxygen content fluctuating, turbid

# FIGURE 5. Brook around 1960 (Dinkel)

# FIGURE 6. Brook around 2000 (Vechte, Germany)

# 3. The regional water management: in the Netherlands

The organisation of regional water management in the Netherlands is very special. The organisation model in which water-boards and provinces and not the state are dominating, is unique.

## The water-boards (nowadays 26) exist since the middle-ages and are even older than the (12) Dutch provinces. Whereas the provinces are based on broad political issues and the political working out of these themes are water-boards only in charge with water management issues. Because of their history the water-boards are dominated by agricultural interests. During two last decades the themes of water-boards evaluated, from water quantity to integral approach, and the number of water-boards decreased significantly.

The modern water-board has following tasks:

## Actual task: water of good quality at the right place at the right moment; originally only determined by agricultural and urban standards for discharge and storage, nowadays on basis of compromises with nature conservation requests;

## Protection against flooding (dikes, storage of superfluous water);

## Protection against drought and against too wet situations (construction and maintenance of water courses); first with highest priority for agriculture and built-up areas, nowadays a compromise of agriculture, cities and nature;

## Protection and improvement of water quality (water treatment, monitoring); a task introduced with the Law against Pollution of Surface water (1970), originally carried out by (new) water quality water-boards., nowadays by the 26 integral water-boards.

## The water policy of European Union (directives in the field of water management), the Dutch state (especially the ministries of environment respectively public works and water management) and provinces determine the aims and the framework of water management plans of water-boards

# 4. Long-term research of aquatic macrophytes in Dutch brooks 1970 - now

## The Working-group Dutch Brooks has been initiated in 1970. This working-group which originally focussed on the brooks in the Southern Netherlands has been founded by two plant-ecologists (Bert Maes + Erik van Dijk). Between 1971:and 1975 the Central and Eastern parts of the Netherlands were added to the research area, whereas the number of active researchers increased to 20 (professionals + volunteers). Originally macrophytes and evertebrate animals were sampled, later the focus became more on only macrophytes. Since 1985 there are about 10 researchers, mainly volunteers, who focus on the monitoring of many permanent sampling plots in the Netherlands and references (Belgium, Germany, Poland). In the monitoring programme the aim is 1 sample per 4 years.

# The aims of the working group are as follows:

## More attention to brooks and especially aquatic macrophytes as “forgotten group”;

## Enlarging ecological knowledge about floating macrophytes in running water;

## Monitoring macrophytes in most natural brooks (some remains) and other brooks;

## Special activities to protect threatened brooks and rare macrophytes (NL: red-list-species, EU: Natura 2000)/

# The methodology of the monitoring of the working group evaluated since 1970:

## Originally small sampling plots (10 m2) and assessment according to scale of Braun-Blanquet;

## After 1980 sections of 30 – 100 m according to Domin-scale (decimal Tansley-scale) with uniform forms (see annex 1);

## Central database of more than 1,600 releves (TurboVeg);

## Building up of a large herbarium of aquatic macrophytes (Utrecht).

# Especially in the beginning the systematic of species found in brooks was a large problem. In flowing water many species hardly produce flowers and seeds which are essential for determining the species. Following facts were bottlenecks in the beginning:

## Specific shapes of submerse plants of brooks caused by water flow (juvenile shapes without flowers / fruits, no emerse or floating leaves);

## English and German determination keys appeared to work better than Dutch ones for field research;

## Determination of Callitriche-species (microscopic research of pollen)

## Determination Nitella / Chara

# At this moment there is a Turboveg-database containg the results of more than 1600 sampling plots situated in more than 250 Dutch brooks). This database is characterized by:

## Most plots are situated in southern, central and eastern Netherlands

## After 1985 2 kinds of plots:- can be distinguished:

### Monitoring (every 4 years)

### Atlas-project (new and probably high-quality brooks)

## Free use of material by other organisations (Floron, RIVM, Alterra, STOWA, Limnodata, waterboards, provinces); only commercial consultants must pay.for the use of data.

In Annex II all species observed in Dutch brooks during 1970 – 2008 are presented.

# The geographic distribution of the most frequent and ecologically most sensitive species has been studied by preparing distribution maps.

Next figure (7) presents the distribution of Potamogeton polygonifolius, a species looking very much like Potamogeton natans but with preference for much lower nutrient contents in water and subsoil. P. polygonifolius once was a general species but dye to nitrification this species has become very rare, especially in brook systems. Only in oligo- mestrophic parts of brook systems –upstream in nature areas- we still can find this species.

FIGURE 7 (red points: presence of P.polygonifloius; black crosses: all sampling plots).

A first evaluation of the distribution maps of all aquatic macrophytes observed during the period 1970 – 2008 lead to the conclusion that especially the aquatic plant species which are dependent on high velocities in water systems like brooks, respectively on low nutrient loads and on non-turbid water generally decreased whereas the occurrence and abundance of species of stagnant water and with quick and high growth in nutrient-rich water significantly increased.

# Further ecological analyses carried out

# Response-analyses by RIVM (Dutch State Institute for Environment and Health) -> autecological response curves

# Simple uni- and bi-variate analyses of some of the most sensitive and most hetened species (Nitella flexilis, Luronium natans)

For further statistical analyses and multivariant analyses a future cooperation with one or more universities appears to be necessary.

5. Changes of species composition 1970 - now

## In tis paper only few more or less representative cases can be presented, a first one in the south of the Netherlands (border with Belgium) and three saples within one brook in the Veluwe area (central Netherlands).

Brook: Tongelreep (plot: Achelse Kluis) Year ‘88 ‘90 ‘97 Cover of vegetation (%) 70 30 2 Elodea nuttallii 5 3 . Ranunculus penicillat. 7 . . Ranunculus peltatus . 3 . Ranunculus fluitans . 3 . Callitriche platycarpa 7 5 . Callitriche spec. . . 3 Callitriche obtusangula . 5 . Potamogeton crispus 5 5 1 Potamogeton pectinatus 9 7 . Potamogeton trichoides . . 4 Sparganium emersum 5 3 .

Brook: Staverdense/Hierdense beek. Three permanent sampling plots 1973 - 2001 Plot 1. Leemkuilen Year 1973 1995 2001 Callitriche hamulata 1 2 . Myriophyllum alterniflorum . 6 1 Potamogeton alpinus . 5 . Callitriche spec. . 6 1 Potamogeton natans . 3 . Ranunculus peltatus . 2 . Nitella flexilis . 1 . Berula erecta . 2 . Plot 2: Castle Staverden) Callitriche hamulata 3 . 1 Elodea canadensis 1 . . Lemna trisulca 1 . . Batrachium species 1 . . Callitriche platycarpa . 2 3 Myriophyllum alterniflorum . 6 6 Berula erecta . 3 3 Callitriche obtusangula . . 3 Plot 3. Zwolse brug Myriophyllum alterniflorum 2 7 6 Apium nodiflorum 1 . . Callitriche hamulata 1 . . Callitriche obtusangula . 3 . Berula erecta . 3 . Elodea canadensis . . 1 Ranunculus peltatus . . 4

# In these cases it is clear that the water vegetations studied on the scale of 50 meters sections are very  dynamic. Only on basis of periodic sampling in hundreds of brooks general trends for plant species and vegetation structure can be derived.

# 5a. Overall survey 1970 – 2008

On basis of comparisons of the occurrence and abundance of all species observed during three periods of observations (1970 – 1980, 1981 – 1995, 1996 – 2008) following significant declines respectively increases of species could be seen.

| Significant decline | Significant increase |
| --- | --- |
| Callitriche stagnalis Luronium natans Myriophyllum alterniflorum Potamogeton alpinus Ranunculus peltatus var. Heterophyllus Ranunculus fluitans Elodea canadensis | Callitriche obtusangula Potamogeton trichoides Elodea nutalli |

# 5b. Preliminary conclusions 1970 – 2008

## Within the management of Dutch brooks large changes occurred during last 30 years. Sanitation measures were carried out for the most polluted brooks, especially those which are influenced by built-up areas: waste water treatment plants have been constructed and/or improved and large restoration projects were carried out to improve the hydromorphology and hydrology of complete brook systems. At the other hand during the same period detoriation and complete disappearance of originally natural situations locally still occurred because of agricultural measures and the continuing load of nutrients coming from agricultural fields. Generally brooks became more turbid during last thirty years and because of decreased velocities of the water in the brooks organic sedimentation increased causing larger fluctuations of oxygen content and changes of the substrate for roots.

## The effect of ll these factors was that the originally wide-spread typical plant species of running and clean water became rare. Especially submerse macrophytes became more rare whereas species with surface leaves and with emergent leaves increased in number and abundancy. The changes in the downstream parts of the brooks were more signifcant than the changes observed in the upstream parts

## In general the development of submerse vegetations can be described  as going from a “black and white” situation - with brooks with a very bad and brooks with a very good status -  to a “grey” overall situation: the range of ecological status narrowed strongly to bad – good. The extreme situations vanished at both sides of the range so that the local revival of ever completely dead rivers as well the further decline of rivers with highest (nature) value could be observed. The extreme bad situations where no submerse plants could occur at all, changed to less bad situations because of the sanitation of point sources carried out according to a nation-wide programme initiated by the Ministry of Environment. But at the other hand there was an increasing effect from further intensification of agriculture causing increasing nutrient loads and further disturbance of the hydrology of brook valleys. Besides the management and maintenance of rivers for macrophytes is still suboptimal; the mowing of vegetation to enable maximum discharge capacities of the brooks is generally too frequent to enable the sustainable presence of most natural vegetations including the more senitive species.

## Alas, for the Dutch brook vegetation new threats an be mntionned:

### - The lowering of aims concerning nutrient loads and nutrient concentration, introduced during the Dutch implementation of the EU Water Framework Directive. Dutch politicians and water managers used the change from duty of effort to the (European) duty of results (monitoring of meeting of standards) as agument for a strong lowering of standards.

### - Within the measures elaborated within the framework of the implementation of the WFD in many places forestation of banks is foreseen. For some sensitive macro-evertebrates this is a positive measure but the shadow will prevent an optimal development of natural submerse vegetations.

### - With some projects to promote fishes, especially trout and salmon, the artificial introduction of pebble substrate instead of th original sandy subsoil has been advised; this is contrary to the interest of natural vegetation developments.

### - Because of the use of Asian, Australian and American plant species in garden ponds an Increasing introduction of exotic plant species in Dutch nature, including its brooks, can be observed.

# 6. EU Water Framework Directive (WFD) and brook vegetation: a new positive perspective?

### Some of the effects of this directive which was established: in 2000, are already mentioned in the above text. A good reason to look more specifically at this new directive, its implementation in the Netherlands and its possible effects for Dutch brooks, more specific the brook vegetations..

### Main aims of this directive with its ecological base are:

### restoration of natural water systems,

### sustainable use and profits of water systems and

### transparant and integral water management.

### The base and the main text of the WFD are promising for making water systems more sustainable:

#### the ecology of water systems is a leading priciple;

#### the minimum aims and efforts are base don the stand-still principle;

#### if there is not enough knowledge the precaution principle is working;

#### the cost-benefit principle as another base of the WFD should lead to limitation of water use and to avoidance of excess use of water and water systems;

#### there are rules for the transparancy of decisions which enables citizens and European Commission to check the national and regional implementations of the WFD;

#### there is a duty to reach objective results (strict standards, criteria developed in guidelines) before strict deadlines (preferably 2015, with clear arguments derogation until 2021 respectively 2027);

#### the working out and monitoring of measures on basis of well-defined “waterbodies”.

Other factors limited the optimism for quick and large ecological restoration of water systems. These factors are connected with determining of status, (too) detailed administrative instructions and the method to distinguish water bodies as the basic element for WFD-policy.

### (1) Within the national implementation of the WFD the national authorities had the task to determine the “status” of every water body. This status at his turn is determining the specific aims and standards in the concerning water body. There are three classes of status: natural, heavily modified respectively artificial. In this order the ecological aims vary from very strict to least strict. In the Netherlands the status natural is very rare because of the predominance of agricultural interests and protection against floods with the Dutch politicians.

### (2) The WFD includes very detailed instructions, not only about aims and monitoring but also how to distinguish water bodies, how to produce river basin management plans, how to do economical analyses. Therefore very many large paper products have to be made before the execution of measures in the field can start. In the Netherlands this has lead to a delay until five years for many high-quality programmes and measures initiated already before the establishment of the WFD.

(3) The WFD-instructions how to distinguish water bodies (on basis of minimum sizes of lakes and with brooks and rivers of catchent areas) lead to the bizarre situation that in the Netherlands watertypes with highest natural values are neglected with the elaboration of WFD-measures whereas the focus for measures became on sections of brooks and rivers with lowest ecological opportunities. In following table his is illustrated.

| Dominant watertypes | Neglected watertypes |
| --- | --- |
| Rivers Small rivers Canals Canal-rivers Lakes | Springs Ditches (peat, sand, clay) Fens Peat-bog lakes River ponds |

# 6a. Aquatic macrophytes and WFD

Following facts can be mentionned about  the relation between (vegetations of) aquatic macrophytes and the WFD and other EU directives:

## The basic WFD-Instruction to determine geographic water bodies (catchment areas larger then 10 km2) leads to the neglecting of small but ecologically most promising water systems (upstream brooks, springs)

## The chemical and ecological aims have been lowered because of EU duty of results (before: national aims on basis of duty of effort)

## No Dutch brook got the WFD-status “natural”, therefore the ecological aim is lower than the Good Ecological Status

## Macrophytes are one of 3 (4) WFD groups of organisms to be assessed and monitored (every 6 years per waterbody)

## Luronium natans is a Natura2000 species. Therefore not only the WFD is important to protect this species but also the EU Habitat Directive leads to the duty of special attention for the maintenance of this plant species which asks for iron-rich and nutrient-poor seepage of watr systems.

# 6b. Measures intended for small rivers on basis of WFD

## Until 2015 in the Netherlands following measures to improve the ecological situation of brooks are foreseen in order of priority:

## Improving of length profile (in general re-meandering);

## Restyling of profile of cross-sections: “nature-friendly” banks;

## Removing of bottlenecks of the migration of fishes: replacement of solid weirs by more natural water-level elevating elements;

## Substrate (digging out of organic sediments);

## Shadowing of brook sections by trees along banks;

## Improvement of maintenance (to guarantee minimum discharge capacities).

## Between 2010 – 2040 two extra programmes of measures will be carried out:

## Improvement of the discharge regime of brooks;

## Lowering of nutrient loads.

For the submerse aquatic plants especially the measures 4, 6, 7 and 8 will be positive (stimulating rare and sensitive species). Measure 5 will be negative for aquatic plants but locally positive for macro-evertebrates.

Modelling of the effects enables only rough assessments of the future vegetation. The case of one special species (Luronium natans) makes clear that uniform measures carried out within the framework of European directives, may result in losses of Luronium populations instead of the increase of this endangered species.

7. Case: Luronium natans

Luronium natans is a worldwide rare plant species. Its distribution is restricted to the Atlantic area of Western-Europe between Northern-Spain, Great-Brittany, Southern-Scandinavia and Poland. In the Netherlands an important part of the world population of this species is still present but during last decennia the number of habitats dropped so that the species is restricted to the eastern and southern regions with sandy soils. Especially in some brooks in the south (Grote Beerze, Kleine Beerze, Reusel a.o.) some large populations are still present (Jansen & Schaminee 2004). In brooks Luronium natans is a species within Potametea-associations, in fens of sandy heather biotopes the species is an element of Littoreletea-associations. Species which in brooks often occurred together with Luronium are for example Myriophyllum alterniflorum, Utricularia australis and Scirpus fluitans, which decreased even more strongly than Luronium during last decades.

Because its restricted distribution in the world and the decreasing presence of large populations of Luronium natans this species is assumed as a threatened species by the European Commission and as such mentioned in annexes II and IV of the European Habitat Directive (species no 1831). This means that the Dutch government is responsible for the protection and good maintenance of habitats of Luronium natans.

Jansen & Schaminee (2004) mention the main circumstances which are important for the survival of Luronium natans in its habitats:

- non-turbid water, low concentrations of phosphate and calcium, very low to medium concentrations of nutrients;

- high potential of dissemination by seeds and by broken parts of plants (often wide spontaneous spread in pioneer situations at dynamic places; seeds are still germinating after 80 years);

- little strength for the competition with other plant species (sometimes dependent on artificial maintenance of habitat vegetation).

For 61 habitats in Dutch brooks Bloemendaal & Roelofs (1988) mention following averages of the P-concentration: P-total 0.036 mg/l, PO4’’’ 0.002 mg/l (maximums: P-total 0.144 mg/l, PO4’’’ 0.019 mg/l).

De Lyon & Roelofs (1986) mention that Luronium natans is very sensitive for the water-type of its habitat. It disappears quickly from places where a bog type of water (sulphate dominance, nutrient-poor soil and water) is replaced by a chloride type or carbonate type of surface water. In the Netherlands this change of water type was a rather common phenomenon during last decades: brooks became into use for the transport of water from larger rivers like Rhine and Meuse for agricultural use in spring and summer time (irrigation). Sometimes the natural values of brooks including their populations of Luronium natans ans Myriophyllum alterniflorum were destroyed for purposes of nature conservation (example: Kleine Beek in Southwestern-Netherlands): transport of river water to a bog to restore its original groundwater level to prevent damage of groundwater dependent vegetations by dessication.

Table X gives an example of the chemical effects of changing the water-type in brooks where Luronium natans and 7 accompanying (rare) plant species disappeared.

| Table X. Chemical changes in brooks around Mariapeel before and after extinction of Luronium natans and accompanying rare plant species “) |
| --- |
|  | Original watertype WITH Luronium natans (before 1970) (n=8) | Changed watertype WITHOUT Luronium natans (after 1970) (n=4) |
|  | Range | Average | Range | Average |
| Salinity | 2.0 – 8.6 | 4.6 | 6.9 – 13.8 | 12.0 |
| Chloronity | 0.3 – 1.7 | 1.0 | 1.7 – 4.0 | 3.3 |
| Alkalinity | 0.1 – 1.8 | 0.7 | 2.5 – 3.5 | 3.0 |
| pH | 4.4 – 7.1 | 5.9 | 7.5 – 8.5 | 7.8 |
| Preference | sulphate (n=5) |  | chloride (n=2) / carbonate (n=2) |  |
| Trophic status water (PO4) | 0.0 – 0.7 | 0.3 | 1.2 – 5.3 | 4.0 |
| Trophic status subsoil | 4.7 – 17.7 | 9.2 | 12.3 – 16.8 | 14.4 |
| Redox potential | (-68)+63 - + 110 | +64 | -122 - -199 | -171 |

‘) Vegetation before 1970: Apium inundatum, Sparganium minimum, Glyceria fluitans, Utricularia minor, Scirpus fluitans, Luronium natans a.o..

Vegetation after 1970: Myriophyllum spicatum, Ceratophyllum demersum, Lemna minor, Utricularia vulgaris.

Modern water managers try to avoid strong changes of water types in brooks such as shown above. For brooks with high natural values no transport of outside-system water is foreseen at the moment. But even now populations of Luronium natans are threatened. Strange enough some of these threats come from planning to make the Dutch brooks more nature friendly (….).

In most habitats of large populations of Luronium natans which still exist in the Netherlands, seepage of iron-rich groundwater can be observed. This iron can fixate phosphorous in the surrounding agricultural fields to a large extent so that the water and the subsoil in the brook where Luronium natans is present has relatively low concentrations of phosphate.

On basis of the EU Water Framework Directive the planning is to restore original benches in most brooks and to construct “nature-friendly” banks. Especially for brooks where maize fields are situated very nearby, causing sub-soils and groundwater saturated with phosphates and nitrates during last 20, 30 years, this is a dangerous measure if Luronium natans must be protected as well. Measures must be carried out quickly because of available subsidies without sufficient basic knowledge of the hydrology and chemistry of the subsoil along the brooks concerned.

# 8. Perspective brooks and floating macrophytes

## In the EU Water Framewk Directive clear aims for aquatic macrophytes are mentioned. Measures to improve the status of this organism group are obligatory and monitoring to assess the progress must be done every three years. However, in the Netherlands long-term aims for fishes and macrozoobenthos (water insects) appeared to be dominating in the working out of short-term aims and with the elaborating of field measures

## Further it is clear that the Dutch elaborating of European Natura 2000 aims such as for threatened plant species Luronium natans focus preferably on isolated stagnant waters, not for open flowing systems where originally many rare plant species occurred.

## More specific following facts can be mentioned for the elaboration of Water Framework Directive aims into concrete measures in the Netherlands:

### There seems to be a (too) strong focus on hydromorphology measures (like restoration of old meanders and the construction of rather uniform “nature-friendly” banks) within downstream sections of brooks. The from ecological viewpoint more promising upstream systems are strongly neglected even when they partly determine the status of the downstream sections of brooks;

### The planning of more wood and shrubs along banks of brooks is probably positive for macro-evertebrates and fishes but negative for the occurrence of aquatic macrophytes;

### The removing of many weirs may stimulate fish migration but seems to be indifferent for macrophytes;

### Many uniform measures (Waternood to decrease dessication, nature friendly banks) will result in decreases of regional differentiation;

### During the next decade only few extra measures to limit diffuse nutrient sources will be carried out. This prevents a quick restoration of the vegetation of relatively sensitive aquatic macrophytes.

### There is not enough attention for water velocity and groundwater seepage to protect relatively rare flow-indicating plant species

### The Water Framework Directive is an instrument which in the Netherlands has lead to a too administrative elaboration. During approx. five years already running programmes for ecological restoration of brooks have been strongly delayed. Further the Dutch working out of the European aims lead to contradicting results:

#### Geographically the main focus has become on measures for large downstream water bodies (downstream sections of brooks) which are ecologically least promising. Measures carried out in these sections has a relatively low effectiveness whereas the Water Framework Directive clearly requests high effectiveness; The neglecting of upstream water systems with highest ecological potentials which had high interest in the Dutch water policy which was carried out before the implementation of the Water Framework Directive, may result in an overall detoriation of ecological values of Dutch water systems instead of an overall restoration.

#### With the choice for possible measures the main focus has become the executing of measures to improve the hydromorphological status of water bodies such as sections of brooks. Re-meandering and constructing of nature-friendly banks can be  seen as end-of-pipeline measures whereas Europe firstly asked for measures at the beginning of the pipeline (decreasing of ischarges of nutrients and pollutants, hydrological restoration of water systems).

#### The high focus on actual agricultural interests with the WFD implementation has lead to a strong delay of the reduction of the nutrient loads into Dutch water systems. This nutrient load is especially for the aquatic macrophytes in all water systems and for macro-evertebrates and fishes in stagnant water systems the most important ecological key factor. The neglecting of this key factor will make a reasonable restoration of water vegetations even in 2027 (ultimate deadline) impossible.

#### There is another delay of the restoration of hydrological water systems around brooks (groundwater fluxes, quantity and quality of seepage into brooks). Here too the high priority for agricultural interests but also for the interests of drinking water supply can be assumed to be the main reason of the delay.  This delay  makes it even more plausible that in 2027 ecologically healthy water systems can ot be expected in 2027.

## On basis of the above mentioned argumentation the expectation for the Dutch brooks in 2027 is that they will be improved  especially as for hydromorhology, valley systems such as floodplains along banks and outdoor-recreation criteria. For the surface water of the brooks general improvements regarding fishes and maco-evertebrates will be obtained whereas the vegetation in brooks will generally stabilize and only locally improvements are plausible. Until 2027 in many cases a further detoriation of aquatic macrophytes is quite possible which is contrary to the basic requests of the European Water Framework Directive and of the Habitat Directive.

## References

Anonymous, 2007. Nederland later; Tweede duurzaamheidsverkenning. Deel: Fysieke leefomgeving Nederland (Future of the Netherlands; second survey of a sustainable development. Part: Physical environment). Milieu en Natuur Planbureau, Bilthoven.

Bloemendaal, F.H.J.L. & J.G.M. Roelofs (eds.), 1990. Waterplanten en waterkwaliteit (Aquatic macrophytes and water quality). KNNV, Utrecht.

Jalink M.H., & A.J.M. Jansen, 1995. Indicatorsoorten voor verdroging, verzuring en eutrofiëring van grondwaterafhankelijke beekdalgemeenschappen (Indicator species for dessiccation, acidification and eutrophication of groundwater dependant ecosystems of brook valleys). Staatsbosbeheer, Driebergen.

Janssen, J.A.M., & J.H.J. Schaminee, 2004. Europese Natuur in Nederland; Soorten van de Habitatrichtlijn (European nature in the Netherlands; Species of the EU Habitat Directive). 146 oo. KNNV, Utrecht.

Jasperse, P., 1997. Beekherstel in Nederland: Voortmodderen met grondverwerving (Restoration of brooks in The Netherlands; multidisciplinary research on restoration and acquiring of grounds needed). 205 pp.. Ph. D. Thesis, Twente University, Enschede.

Ligtvoet, W. (ed.), 2008. Kwaliteit voor later; Ex ante evaluatie Kaderrichtlijn Water (Quality for later; ex ante evaluation of Water Framework Directive). 212pp.. Milieu en Natuur Planbureau, Bilthoven.

Lyon, M.J.H. de, & J.G.M. Roelofs, 1986. Waterplanten in relatie tot waterkwaliteit en bodemgesteldheid (Aquatic macrohytes in relation to water quality and soil conditions). Two parts. Katholic University, Nijmegen.

## Nijboer, R., 2006. The myth of communities. Determining ecological quality of surface waters using macroinvertebrate community patterns. Wageningen University. Alterra Scientific Contributions no 17. Wageningen.

Sculthorpe, C.D., 1871. The biology of Aquatic Vascular Plants. 610 pp.. E.Arnold, London.

Verdonschot, P. (ed.), 1995. Beken stromen; Leidraad voor Ecologisch beekherstel (Brooks water is streaming; Handbook for the ecological restoration of brooks). 236 pp. Stowa 95-03 / WEW-06. Utrecht.

Verdonschot, P. (ed.), 2000. Natuurlijke levensgemeenschappen van de Nederlandse binnenwateren. Deel 2, Beken (Natural ecosystems of Duitch fresh surface waters. Part 2: Brooks). 128 pp. Expertisecentrum, Ministry of Agriculture, Nature and Fisheries. Report AS-02. Wageningen.

Vlies, M. van der, 1996. Beken natuurlijk in beweging; Werken aan schoon, slingerend en stromend water (Brooks naturally moving; Working on clean, dynamic and flowing water) . Vogelbescherming Nederland, Zeist.

Wassink, W.Th., 1999. Beekdallandschappen; een morfologisch onderzoek in de zandgebieden van Nederland (Landscapes of brook valleys; Morphological research in sandy areas in the Netherlands).232 pp..  Ph.D. thesis, Wageningen University.

Weber-Oldecop, D.W., 1969. Wasserpflanzengesellschaften im östlichen Niedersachsen (Communities of aquatic macrophytes in eastern Lower-Saxonia, Germany). 171 pp, Ph.D. thesis, Hannover.

ANNEX I

Standard form for observations on aquatic macrophytes per sampling plot in Dutch brooks

Name of brook  ……………………………………………….	Location  …………………………

Date and nr yymmddnn   .. .. .. .. .. .. .. ..			Old date and nr yymmddnn   	.. .. .. .. .. .. .. ..

Observation by  ………………………………………..		Municipality 	…………………………………..

Province/country  	.. ..		Substrate 	B-T-S-V	 Source of pollution	         0-1-2-3-4-5-6-7-8-9

Nr of map	    	.. .. ..	Sapropelium

min		.. .. 	cm	  Organic pollution		0-2-3-4-5

Coordinates EW  	.. .. .. , .. ..	average		.. ..	cm	  Reconstruction		0-2-3-4-5

Coordinates NS		.. .. .. , .. 	max		.. .. 	cm	  Mowing (maintenance)	0-2-3

Landscape			Seepage	O-Y-B-M-U	  	  Weirs			0-1

Accompanying elements  0-8		Smell (1)	O-S-R-Y-F-A	  	  Sampling plot - length 	.. .. ..	m

Shadow		0-4		Smell (2)	O-B-Z-G-GR-W-Y-GY	  - width	 		.. .. ..	m

Width		.. ..  	m	Turbidity 	H-M-T	  	  Vegetation cover total	.. ..	%

Depth	min	.. .. .. 	cm	Visibility bottom  	0-1			helophytes 	.. ..	%

average	.. .. .. 	cm	Velocity (measurement).. .. , ..m/s		floating 		.. ..	%

max 	.. .. .. 	cm	Velocity (estimation) 	0-4		submerse 	.. ..	%

Bank inclination	1-4		Conductivity	.. .. .. ..	mS/cm	   Sampling method		T-B-L-M-S-K-V

Bank height 	.. .. , .. 	m	pH		.., ..		   Extra observations	+ / -

Soil surface	Z-G-K-V-L	Pollution / yr	.., .. ..				   (see other side of form)

| Acorus calamus |  |  |  | Juncus bulbosus |  |  |  | Potamogeton obtusifolius |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Agrostis stolonifera |  |  |  | Juncus effusus |  |  |  | Potamogeton pectinatus |  |  |  |
| Alisma plantago aquatica |  |  |  | Lemna gibba, vlak |  |  |  | Potamogeton perfoliatus |  |  |  |
| Alopecurus geniculatus |  |  |  | Lemna gibba, bol |  |  |  | Potamogeton polygonifolius |  |  |  |
| Apium inundatum |  |  |  | Lemna minor |  |  |  | Potamogeton pusillus |  |  |  |
| Apium nodiflorum |  |  |  | Lemna cf minuscule |  |  |  | Potamogeton trichoides |  |  |  |
| Berula erecta |  |  |  | Lemna minuscule |  |  |  | Ranunculus aquatilis |  |  |  |
| Butomus umbel. beekvorm |  |  |  | Lemna spec |  |  |  | Ranunculus circinatus |  |  |  |
| Callitriche hamulata |  |  |  | Lemna trisulca |  |  |  | Ranunculus flammula |  |  |  |
| Callitriche obtusangula |  |  |  | Leptodictyum riparium |  |  |  | Ranunculus fluitans |  |  |  |
| Callitriche platycarpa |  |  |  | Luronium natans |  |  |  | Ranunculus hederaceus |  |  |  |
| Callitriche spec |  |  |  | Mentha aquatica |  |  |  | Ranunculus peltatus |  |  |  |
| Callitriche spec/broad leaves |  |  |  | Myosotis laxa |  |  |  | Ranunculus pseudofl |  |  |  |
| Callitriche spec/narrow l. |  |  |  | Myosotis palustris |  |  |  | Ranunculus repens |  |  |  |
| Callitriche stagnalis |  |  |  | Myosotis spec |  |  |  | Riccia fluitans |  |  |  |
| Cardamine amara |  |  |  | Myriophyllum alterniflorum |  |  |  | Rorippa amphibia |  |  |  |
| Cardamine pratensis |  |  |  | Myriophyllum spicatum |  |  |  | Rumex hydrolapathum |  |  |  |
| Ceratophyllum demersum |  |  |  | Myriophyllum verticillatum |  |  |  | Sagittaria sagittifolia |  |  |  |
| Chara spec |  |  |  | Nasturtium officinale |  |  |  | Sagit.sag.f.vallisneriifolia |  |  |  |
| groene draadwieren |  |  |  | Nasturtium microphyllum |  |  |  | Scirpus fluitans |  |  |  |
| Eleocharis acicularis |  |  |  | Nasturtium spec |  |  |  | Scirpus lacustris |  |  |  |
| Eleocharis palustris |  |  |  | Nitella flexilis |  |  |  | Scirpus lac. brook form |  |  |  |
| Elodea canadensis |  |  |  | Nuphar lutea |  |  |  | Sparganium emersum |  |  |  |
| Elodea nuttallii |  |  |  | Nymphoides peltatus |  |  |  | Sparganium erectum |  |  |  |
| Elodea spec. |  |  |  | Oenanthe aquatica |  |  |  | Sphaerotilis |  |  |  |
| Equisetum arvense |  |  |  | Phalaris arundinacea |  |  |  | Spirodela polyrhiza |  |  |  |
| Equisetum fluviatile |  |  |  | Philonotis fontana |  |  |  | Veronica anagallis-aquatica |  |  |  |
| Equisetum palustre |  |  |  | Phragmites australis |  |  |  | Veronica becca-bunga |  |  |  |
| Fontinalis antipyretic |  |  |  | Platyhypn. riparoides |  |  |  | Veronica catenata |  |  |  |
| Glyceria declinata |  |  |  | Polygonum amphibium |  |  |  | Zannichellia palustris |  |  |  |
| Glyceria fluitans |  |  |  | Polygonum hydropiper |  |  |  | …… |  |  |  |
| Glyceria fluit. brook form |  |  |  | Potamogeton acutifolius |  |  |  | …… |  |  |  |
| Glyceria maxima |  |  |  | Potamogeton alpinus |  |  |  | …… |  |  |  |
| Glyceria max. brook form |  |  |  | Potamogeton berchtoldi |  |  |  | …… |  |  |  |
| Hottonia palustris |  |  |  | Potamogeton crispus |  |  |  | …… |  |  |  |
| Hydrocharis m.-ranae |  |  |  | Potamogeton lucens |  |  |  | Heading data into form |  |  |  |
| Hydrodictyon reticulata |  |  |  | Potamogeton mucronatus |  |  |  | Check |  |  |  |
| Iris pseudacorus |  |  |  | Potamogeton natans |  |  |  | Plant data into form |  |  |  |
| Juncus articulatis |  |  |  | Potamogeton nodosus |  |  |  | Check |  |  |  |

SECOND PAGE OF STANDARD FORM:

VEGETATION ON BANK:

MAP OF SITUATION:

MACROINVERTEBRATES:

SPECIAL REMARKS:

SAMPLED PLANTS (FOR EXTRA DETERMINATION OF SPECIES):

The scales used for abundance per plant species for the various sample techniques Visser: only macrophytobenthos):

# TANSLEY		BRAUN BLANQUET		LONDO			MAES

1 = s   = rare		1 =  <5%, 4 or less specimens	1    = < 1 %		1 = very few

2 = r   = scarce or 	2 =  <5%, upto 2 specimens	2    = 1 – 3%		2 = few – rather many

very spreaded	3    = 3 – 5 %			3 = many

3 = o   = here and there	3 =  <5%, approx. 3-10 specimens	10  = 5 – 15 %		4 = extremely many

4 = lf  = locally frequent	4 =  <5%, more than 10 specimens	20  = 15 – 25 %

5 = f   = frequent		5 =  5   - 12%			30  = 25 – 35 %		VISSER

6 = la  = locally very many  6 =  13 - 25%			40  = 35 - 45 %		1 = 1 - 2

7 = a   =  very many	7 =  26 - 50%			50  = 45 – 55 %		2 = 2 - 10

8 = cd = codominant	8 =  51 - 75%			60  = 55 – 65 %		3 = 10 - 50

9 = d   = dominant	9 =  76 - 100%			70  = 65 – 75 %		4 = > 50

80 = 75 – 85 %

90  = 85 – 100 %

QUALITATIVE ESTIMATION : 0 = absent / 1 = present

ANNEX II: Species of aquatic macrofytes observed in Dutch brooks (1970 – 2005)

| NRSL SCIENTIFIC NAME | NRSL SCIENTIFIC NAME |
| --- | --- |
| 0007 Acorus calamus 0019 Agrostis capillaris 0018 Agrostis stolonifera 6017 Alisma 0027 Alisma lanceolatum 0028 Alisma plantago-aquatica 0036 Alnus glutinosa 0040 Alopecurus geniculatus 2512 Amblystegium riparium 0077 Apium inundatum 0078 Apium nodiflorum 0096 Arrhenatherum elatius 1215 Berula erecta 0141 Bidens cernua 0144 Bidens tripartita 0171 Butomus umbellatus 6094 Calamagrostis 6097 Callitriche 0180 Callitriche hamulata 0182 Callitriche obtusangula 0184 Callitriche platycarpa 0185 Callitriche stagnalis 2338 Caltha palustris 6103 Cardamine 0201 Cardamine amara 0205 Cardamine pratensis 6106 Carex 0229 Carex elongata 0249 Carex paniculata 0260 Carex rostrata 0274 Catabrosa aquatica 0299 Ceratophyllum demersum 2153 Chara 2164 Characeae 2131 Draadwier 0429 Echinodorus ranunculoides 0435 Eleocharis acicularis 1914 Eleocharis palustris 1154 Eleogiton fluitans 0441 Elodea canadensis 0442 Elodea nuttallii 6192 Epilobium 0451 Epilobium hirsutum 0453 Epilobium lanceolatum 0462 Equisetum arvense 0463 Equisetum fluviatile 0466 Equisetum palustre 2750 Fontinalis antipyretica 2376 Galium palustre 0582 Glechoma hederacea 0583 Glyceria declinata 0584 Glyceria fluitans | 0585 Glyceria maxima 0991 Groenlandia densa 0630 Hippuris vulgaris 0631 Holcus lanatus 0632 Holcus mollis 0638 Hottonia palustris 0640 Hydrocharis morsus-ranae 0641 Hydrocotyle vulgaris 0665 Iris pseudacorus 0673 Juncus articulatus 0675 Juncus bufonius 2343 Juncus bulbosus 0680 Juncus effusus 6291 Lemna 0722 Lemna gibba 2374 Lemna gibba + minor 0723 Lemna minor 0724 Lemna trisulca 0753 Littorella uniflora 0763 Lotus pedunculatus 0765 Luronium natans 0780 Lycopus europaeus 0782 Lysimachia nummularia 0784 Lysimachia vulgaris 0785 Lythrum salicaria 0813 Mentha aquatica 6352 Myosotis 0841 Myosotis laxa subsp. cespitosa 1922 Myosotis laxa + scorpioides 0844 Myosotis scorpioides 6356 Myriophyllum 0850 Myriophyllum alterniflorum 0851 Myriophyllum spicatum 0852 Myriophyllum verticillatum 6362 Nasturtium 2158 Nitella 2155 Nitella flexilis 0865 Nuphar lutea 0867 Nymphoides peltata 0868 Oenanthe aquatica 0869 Oenanthe fistulosa 0967 Persicaria amphibia 0972 Persicaria hydropiper 0975 Persicaria minor 0976 Persicaria mitis 0929 Peucedanum palustre 0930 Phalaris arundinacea 2866 Philonotis fontana 0933 Phragmites australis 2883 Plagiothecium denticulatum 0957 Poa palustris 0959 Poa trivialis |
| NRSL SCIENTIFIC NAME | NRSL SCIENTIFIC NAME |
| 0860 Rorippa nasturtium-aquaticum 0979 Polystichum aculeatum 6422 Potamogeton 0985 Potamogeton acutifolius 0986 Potamogeton alpinus 0987 Potamogeton berchtoldii 0990 Potamogeton crispus 0993 Potamogeton gramineus 0994 Potamogeton lucens 0992 Potamogeton mucronatus 0995 Potamogeton natans 0996 Potamogeton nodosus 0997 Potamogeton obtusifolius 0998 Potamogeton pectinatus 0999 Potamogeton perfoliatus 1000 Potamogeton polygonifolius 1002 Potamogeton pusillus 1003 Potamogeton trichoides 1619 Potamogeton x fluitans 6437 Ranunculus 1041 Ranunculus aquatilis 1046 Ranunculus circinatus 1048 Ranunculus flammula 1049 Ranunculus fluitans 1050 Ranunculus hederaceus 1055 Ranunculus peltatus 2416 Ranunculus peltatus var. heterophyl 1056 Ranunculus repens 1058 Ranunculus sceleratus | 2900 Rhynchostegium riparioides 3468 Riccia fluitans 1074 Rorippa amphibia 0859 Rorippa microphylla 5201 Rorippa microphylla + nasturtium-aq 1099 Rumex hydrolapathum 1114 Sagittaria sagittifolia 1119 Salix cinerea 1949 Schoenoplectus lacustris 1155 Schoenoplectus lacustris 1160 Scirpus sylvaticus 1167 Scrophularia auriculata 1216 Sium latifolium 1231 Sparganium emersum 1229 Sparganium erectum 3239 Sphagnum recurvum 1241 Spirodela polyrhiza 1248 Stellaria graminea 1247 Stellaria uliginosa 1317 Typha angustifolia 1318 Typha latifolia 6543 Utricularia 1327 Utricularia vulgaris 6551 Veronica 1346 Veronica anagallis-aquatica 1349 Veronica beccabunga 1350 Veronica catenata 1964 Zannichellia palustris |

ANNEX III

Significant floristic changes in Limburg brooks between 1972 and 1990 (n = 2 * 92 ‘) )

| Cover of vegetation (%) | average '70-'71 | average '85-'89 |
| --- | --- | --- |
| helophytes | 1 | 3 |
| Floating leaves at surface | 16 | 4 |
| Submersed leaves | 31 | 24 |
| totaal | 44 | 26 |

| Species which increased | '70-'72 | '85-'90 |
| --- | --- | --- |
| Agrostis stolonifera | 0 | 28 |
| Alisma platago-aquatica | 3 | 8 |
| Alopecurus geniculatis | 0 | 4 |
| Callitriche hamulata | 8 | 20 |
| Callitriche platycarpa | 17 | 44 |
| Cardamine pratensis | 0 | 4 |
| Eleocharis acicularis | 2 | 6 |
| Elodea nutalli | 7 | 23 |
| Glyceria fluitans | 17 | 30 |
| Glyceria maxima | 12 | 21 |
| Leptodictium riparium | 2 | 6 |
| Luronium natans | 0 | 2 |
| Myosotis palustris | 0 | 10 |
| Myriophyllum spicatum | 5 | 8 |
| Nitella flexilis | 4 | 6 |
| Phalaris arundinacea | 4 | 23 |
| Phragmites australis | 2 | 6 |
| Platyhypnidium riparium | 3 | 7 |
| Poa trivialis | 2 | 6 |
| Polygonum hydropiper | 0 | 8 |
| Potamogeton berchtoldii | 0 | 6 |
| Potamogeton natans | 19 | 26 |
| Potamogeton pectinatus | 3 | 7 |
| Potamogeton pusillus | 9 | 12 |
| Potamogeton trichoides | 2 | 20 |
| Ranunculus peltatus | 0 | 3 |
| Ranunculus repens | 0 | 10 |
| Sparganium erectum | 0 | 7 |

| Species which decreased | '70-'72 | '85-'90 |
| --- | --- | --- |
| Callitriche spec. | 11 | 4 |
| Elodea canadensis | 28 | 12 |
| Juncus bulbosus | 2 | 0 |
| Lemna trisulca | 3 | 1 |
| Potamogeton alpinus | 2 | 0 |
| Potamogeton crispus | 22 | 11 |
| Potamogeton perfoliatus | 4 | 2 |
| Ranunculus fluitans | 12 | 8 |
| Ranunculus pseudofluitans | 9 | 5 |
| Sagittaria sagittifolia | 17 | 3 |
| Spirodela polyrhiza | 4 | 1 |
| Zannichellia palustris ssp. palustris | 5 | 0 |

‘) Brooks sampled in alphabetical order (between brackets: number of samples per brook)

Aa (1), Afleidingskanaal (2), Broekhuizer Molenbeek (3), Bronvijvers Wittem (2), Dijkerpeelbeek (1), Eckeltse Beek (2), Everlose beek (5), Geul (15), Grote Molenbeek (5), Gulp (1), Haelense beek (1), Heukelomse Beek (2), Hushover beek (1), Itterse beek (3), Kabroekse Beek (1), Kievitsloop (1), Kroonbeek (1), Leukerbeek (3), Loobeek (=Molenbeek) (1), Maasnielderbeek (3), Noordervaart (2), Oostrumse Beek (3), Oude Graaf (3), Panheelder beek (1), Pepinusbeek (1), Raambeek (1), Rennebeek (1), Riet (=Bosscher Vaart) (3), Roggelse beek (4), Rode beek (Z-Limburg) (1), Slijbeek (1), Swalm (4), Tungelroyse beek (4), Uffelse beek (2), Visschensteert (3), Vlootbeek (4).